Overview of networking
-Access networks
-Physical Media

- Multiple devices managed by router
  - Connected to ISP via modem
- Devices
  - Cabled device
  - Wireless router
  - Router and wirelss access often in one device
- Local area networks
  - Usually with multiple users, webservers, switches, routers, etc
- Wireless
  - Shared wirelss access networks connect end system to router via base station
- Physical media
  - Provide required links between sender and receiver
  - Propgates bits between sender/receiver pairs
- Two type of physical media
  - Guided media – signals propagate in solid media (touch and see)
  - Unguided – propagate freely (wireless)
- Guided media
  - Copper wires
    - Cat 3 – 10Mbps
    - Cat 5 – 100Mbps, 1Gbps Ethernet
    - Cat 6 – 1Gbps, 10Gbps Ethernet
    - Standard sets of connections
    - Connecting computers directly changes the wiring configuration (RJ-45)
  - Coaxial cable
    - Used for main connections
    - Faster than twisted pair
    - Baseband
      - Single channel on cable
      - Legacy ethernet
    - Broadband
      - Multiple channels
      - Uses larger part of wave spectrum
      - Frequency division multiplexing
        - Must be separated
        - Receiver can “tune” into specific frequency
        - Multiple channels
    - Usually less interference
  - Fiber optic cable
    - Glass fiber carrying light pulses, each pulse represents one bit
    - High speed
    - Does not use frequency division multiplexing
    - Channels are colors (specific wavelengths), demultiplexer is similar to a prism
- Unguided media
  - Wireless radio
    - Signal carried in electromagnetic specturm
      - In the air
    - No physical wire
    - Effects of propagation environment
      - Reflection
    - Radio link types
    - Terrestrial microwave
    - LAN
      - 11Mbps, 54Mbps
    - Wide-area (cellular)
    - Satellite